## Slide 1
FloodWatch
Mapping flood damage from space
Case study: Trishuli flood, Nepal, 26 August 2026
Multimodal AI Hackathon 2026 · Track B
Educational prototype, not field-verified
Notes: [0:00–0:20] Hi, we're team [name], and this is FloodWatch, our entry for Track B, Mapping Flood Damage from Space. On 26 August 2026 a flood hit the Trishuli valley in Nepal. We asked: using only free satellite data, how fast can we tell where it hit, what was damaged, and who is cut off? One note up front: this is an educational prototype, and nothing here is field-verified.

## Slide 2
Floods hit fast, and information comes slowly
Where?
Water and debris extent, even under monsoon cloud
What?
Buildings, roads and bridges affected
Who?
Communities cut off from the nearest hospital
Radar sees through clouds, so we build on Sentinel-1.
Notes: [0:20–0:45] After a flood, responders need three answers quickly. Where is the water or debris? Which buildings, roads and bridges are affected? And which communities can no longer reach a hospital? Cloud cover makes optical satellites unreliable in monsoon season, and remote valleys have little ground information. So we built around radar, which sees through clouds.

## Slide 3
How it works
1 Flood mask
Sentinel-1 before (16 Aug) vs after (28 Aug), same orbit. Sentinel-2 skipped: only 11.5% clear.
2 Damage
Pre-event OSM snapshot (27 Jul): buildings, roads, bridges overlapping the mask.
3 Cut-off
Road graph minus flooded segments: who loses the route to a hospital?
Bonus: Copernicus DEM traces the flood path down the valley.
Notes: [0:45–1:25] You give FloodWatch a bounding box and a flood date. Step one: we compare Sentinel-1 radar from 16 August, before, and 28 August, after, same orbit track, so the images are directly comparable. Sentinel-2 optical was only 11.5 percent clear, so the pipeline correctly chose not to use it. Step two: we take buildings, roads and bridges from an OpenStreetMap snapshot dated 27 July, before the event, and count what overlaps the flood mask. Step three: we build a road graph, remove flooded segments, and check which settlements lose their route to a hospital. As a bonus, the Copernicus DEM traces the flood path down the valley.

## Slide 4
Data rules we followed
Inputs: Sentinel-1, Sentinel-2, Copernicus DEM, pre-event OpenStreetMap
No model trained: no training dataset used
EMSR927 reference: final evaluation only, never a pipeline input
Runs from raw data: one run() call in Google Colab
Notes: [1:25–1:45] We kept the data rules strict. Inputs are Sentinel-1, Sentinel-2, Copernicus DEM and pre-event OpenStreetMap. We trained no model, so no training dataset is involved. The Copernicus EMS reference maps, EMSR927, are used only in the final evaluation cell, to check our results afterwards, never as an input.

## Slide 5
What we found
0.07 km²
detected flood area
30 / 2,660
buildings hit (+15 at risk)
0.39 / 192.8 km
road hit
1 / 18
bridges hit
Mask = radar-change (debris-affected) areas only; no open water detected.
Notes: [1:45–2:30] Here are the results for the Trishuli case. The detected flood area is 0.07 square kilometres. Of 2,660 buildings, 30 overlap the mask, and 15 more are at risk. Of 192.8 kilometres of road, 0.39 kilometres is hit. And of 18 bridges, one is hit. Note the mask contains radar-change, debris-affected areas only; no open water was detected.

## Slide 6
Who is cut off?
1
settlement cut off from hospital
24 of 40
settlements analysed
14
no road within 500 m: not assessed
Flood path: 5 settlements listed along the valley, up to ~23 km downstream.
Town access not assessed: no town in OSM data for this area.
Notes: [2:30–2:55] Of 40 settlements, 24 had enough road data to analyse for hospital access. One village sits inside the flood zone and is flagged as cut off from the hospital. 14 settlements had no road within 500 metres, so we can't assess them, and we say so rather than guess. No town exists in the OSM data for this area, so town access was marked as not assessed. The flood-path trace lists five settlements along the valley, out to about 23 kilometres downstream.

## Slide 7
An AI copilot that cannot invent numbers
facts.json
(numbers from maps)
→
LLM writes report
English + Nepali
→
Check every number
against facts.json
→
Rewrite, then fixed
template fallback
The model only sees the facts file, so the report stays grounded in the analysis.
Notes: [2:55–3:25] Our AI component is a situation-report copilot. A language model writes a short report in English and Nepali and answers questions, but it only sees facts.json, a file of numbers computed from the maps. Every number in its answer is checked against that file. If a number isn't there, the answer is rewritten, and if it still fails, we fall back to a fixed template. So the report can't invent figures.

## Slide 8
Honest limitations
Detected area is much smaller than the EMSR927 reference
Results depend strongly on detection thresholds
OSM is thin in remote valleys: cut-off can hinge on one road segment
Satellites revisit every few days: no early warning
Damage is inferred from overlap, not field-verified
Notes: [3:25–3:50] We want to be upfront. Our detected area is much smaller than the EMSR927 reference, so we likely under-detect. Results depend strongly on thresholds: more permissive settings give a much larger area and more cut-off settlements. OpenStreetMap is thin in remote valleys, so cut-off results can hinge on a single road segment. And satellites revisit every few days, so this is not early warning. It's a fast first-look tool, not a replacement for field assessment.

## Slide 9
Next steps
Calibrate thresholds on more flood events
Add richer road data beyond OSM
Validate with field and responder feedback
Thank you · Questions?
Contains modified Copernicus Sentinel data 2026 · © OpenStreetMap contributors
Notes: [3:50–4:00] Next: calibrate thresholds against more events, add more data sources for roads, and validate in the field. Thank you, FloodWatch is open for questions.